## Slide 1
A Methodology for a Decision Support Tool for a Tidal Stream Device
Andrew Cooper
Julen Garcia-Ibanez
Ciaran Gilbert
Stuart Mack
Xabier Miquelez de Mendiluce
29/04/2014
A Methodology for a Decision Support Tool for a Tidal Stream Device

## Slide 2
1
A Methodology for a Decision Support Tool for a Tidal Stream Device
1
Index
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
Wave/ Tidal Interaction Tool
Exceedance Curve Calculation Tool
Blade Element Momentum Analysis Tool
Material Analysis Tool
Techno-Economic Analysis Tool
Introduction
Conclusion
1
2
3
4
5
A Methodology for a Decision Support Tool for a Tidal Stream Device
1

## Slide 3
1
A Methodology for a Decision Support Tool for a Tidal Stream Device
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Background
Why Tidal Stream Energy?
Predictable
Minimal visual and environmental impact
7,743 miles of coastline
Why a methodology for a decision support tool?
Timeframe
Lack of data and other projects feedback
2

## Slide 4
1
A Methodology for a Decision Support Tool for a Tidal Stream Device
Aim
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
To develop a methodology that supports the decision making process of the design of cost-efficient Tidal Stream devices creating, efficient, compact and reliable engineering tools that provide a techno-economic assessment of a tidal energy project
3

## Slide 5
1
A Methodology for a Decision Support Tool for a Tidal Stream Device
Diagram
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Wave/Tidal Interaction
Exceedance Curve Calculator
BEM Analysis
Material Analysis
Techno-Economic Analysis
1
2
3
4
5
4

## Slide 6
Tool calculates the key parameters for a tidal stream device in a site location
Valuable in eliminating sites which do not have the correct velocity characteristics
1
Wave/Tidal Interaction Tool
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
Description
A Methodology for a Decision Support Tool for a Tidal Stream Device
5

## Slide 7
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
1
Wave/Tidal Interaction Tool
Surface Tidal Stream [m/s] Depth of Site [m]
Allowable Change [%]
Wave Height [m]
Wave Period [s]
Inputs
A Methodology for a Decision Support Tool for a Tidal Stream Device
6

## Slide 8
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
1
Wave/Tidal Interaction Tool
Available Region [m]
Hub-Seabed Distance [m]
Outputs
A Methodology for a Decision Support Tool for a Tidal Stream Device
7

## Slide 9
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
1
Wave/Tidal Interaction Tool
Hub Height
Diameter
Available Region
A Methodology for a Decision Support Tool for a Tidal Stream Device
8

## Slide 10
Add 1/7th Power Law to free surface velocity
Calculate wave particle velocity
Calculate wave drift force
Sum the three velocities together
Find region of least variation change with the implementation of a percentage difference
1
Wave/Tidal Interaction Tool
Methodology
Introduction
Tool 3
Tool 4
Tool 5
Conclusion
Tool 1
Tool 2
A Methodology for a Decision Support Tool for a Tidal Stream Device
1/7th Law
Vparticle
Vdrift
9

## Slide 11
Exceedance curve shows the number of days a year the tidal flow rate exceeds speed values
Used to analyse different rates of change at different sites
Important in calculating power output of a system
Probability values are used in further tools
Introduction
Tool 3
Tool 4
Tool 5
Conclusion
2
Exceedance Curve Calculation Tool
Description
Tool 1
Tool 2
A Methodology for a Decision Support Tool for a Tidal Stream Device
10

## Slide 12
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
2
Exceedance Curve Calculation Tool
Inputs
Tidal Stream Input [m/s] Depth of Site [m]
Hub-Seabed Distance [m]
Tidal Shear Law
Entry of site name
A Methodology for a Decision Support Tool for a Tidal Stream Device
11

## Slide 13
Tool 2
2
Exceedance Curve Calculation Tool
Outputs
Exceedance curve [m/s]
Flow probabilities [%]
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
12

## Slide 14
Surface speeds altered for hub depth using 1/7th power law
Adjust the tidal curve to fit a sinusoidal curve
Increase the sampling rate by interpolating between the hourly values of flow rate on the sinusoidal curve
Create 1200 by 100 matrix of flow speeds
Count values to find flow speed distribution
Tool 2
2
Exceedance Curve Calculation Tool
Methodology
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
13

## Slide 15
Divide counted values for each set flow speed by the total number of values to find probabilities
Tidal flow speed distribution curve calculated
Exceedance curve data calculated from probabilities and then plotted as an output
Tool 2
2
Exceedance Curve Calculation Tool
Methodology
Flow Velocity Distribution
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
14

## Slide 16
6
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
Description
A Methodology for a Decision Support Tool for a Tidal Stream Device
HARP_Opt
NREL
Matlab
Blade Element Momentum
Blade Design
Structural Optimisation
Thickness
Genetic Algorithm
Annual Energy Output
Mass
15

## Slide 17
6
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
Inputs
Depth of Site [m]
Hub-Seabed Distance [m]
Turbine Diameter [m]
Flow probabilities [%]
Young’s Modulus [GPa]
Allowable Strain [%]
Material Density [kg/m3]
Blade Family (CD, CL, Geo)
Genetic Algorithm Control
A Methodology for a Decision Support Tool for a Tidal Stream Device
16

## Slide 18
6
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Inputs
17

## Slide 19
14
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
Outputs
A Methodology for a Decision Support Tool for a Tidal Stream Device
18

## Slide 20
Fixed Rotor Speed [rpm] and Fixed Blade Pitch [deg]
Torque [kN-m]
Rotor Power [kW] and Power Coefficient [-]
Stresses [MPa]
Normal and Tangential Bending Moments [kN-m]
15
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
Outputs
A Methodology for a Decision Support Tool for a Tidal Stream Device
19

## Slide 21
11
1. Axial Force
2. Rotating Angular Stream Tube
Momentum Theory
3. Relative Force
4. Blade Elements Drag and Lift
Blade Element Theory
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
Methodology
A Methodology for a Decision Support Tool for a Tidal Stream Device
Genetic Algorithm
20

## Slide 22
11
3
Blade Element Momentum Analysis Tool
Tool 2
Introduction
Tool 1
Tool 3
Tool 4
Tool 5
Conclusion
Methodology
A Methodology for a Decision Support Tool for a Tidal Stream Device
Initial Population
45 Optimum Blades
21

## Slide 23
Quantify the effect of the varying loading profile during rotation of the blade on the design of the blade root
Damage Equivalent Load (DEL) method equates the damage by a spectrum of stress ranges over time to a single value alternating at a single frequency
4
Material Analysis Tool
Description
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
22

## Slide 24
BEM
Tidal
SN Curve
Blade Root
Root bending moments & corresponding flow speed
Flow velocity behaviour at maximum and minimum depth of the blade root
Constants A & B from the equation of line
User-defined geometry & timeframe
Rotational speed of turbine
4
Material Analysis Tool
Inputs
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
23

## Slide 25
Stress Margin
The design of the turbine root is operating within safe limits at positive values
Re-design of the turbine root segment is driven by damage accumulation as the margin approaches zero or reaches negative values.
Chart: Stress Margin
| Alu | GRFP | CFRP
Stress Margin | 28.7 | 58.6 | 82.4
5
Material Analysis Tool
Outputs
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
24

## Slide 26
Root Bending Moments
Stress at Max and Min Depth of Root
Calculate Stress Range & Count Stress ‘Bins’
DEL
Stress Margin (%)
5
Material Analysis Tool
Methodology
Introduction
Tool 1
Tool 2
Tool 3
Tool 4
Tool 5
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
↑Velocity
↓Velocity
25

## Slide 27
Tool 4
Tool 5
11
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
Description
5
Techno-Economic Analysis Tool
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
↓LCoE ?
↓Mass
↑Energy
26

## Slide 28
Tool 4
Tool 5
11
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
Inputs
Material Cost [₤/kg]
Turbine Diameter [m]
Rated Power [kW]
Availability [%]
Efficiency [%]
ROCs CfD Tariff [₤/MW-h]
Discount Rate [%]
5
Techno-Economic Analysis Tool
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
27
Notes: Blade Element Momentum Theory equates two methods of examining how a wind turbine operates. The ﬁrst method MOMEMENTUM METHOD is to use a momentum balance on a rotating annular stream tube passing through a turbine. The second BLADE ELEMENT METHOD is to examine the forces generated by the aerofoil lift and drag coefﬁcients at various sections along the blade. These two methods then give a series of equations that can be solved iteratively.
a=(v1-v2)/v1 (AXIAL INDUCTION FACTOR)
Momentum method……………………………..
1. Axial Force
(Axial Stream tube around a Wind Turbine)
Bernouilli eq AND p1=p4, V2=v3  AXIAL FORCE on the blade
2. Rotating Annular Stream tube
(Rotating Annular Stream tube)
Conservation of angular momentum in the annular stream tube FOR the 4 stations where, blade rotates at GAMMA mayus  TANGENTIAL FORCE on an annular element of fluid  Torque (T) = tangential force * radius
+Tip Lost Correction (At the tip of the turbine blade losses are introduced in a similar manner to those found in wind tip vorticies on turbine blades)
Blade element method…………………..
3. Relative Flow
(Forces on the turbine blade)
Lift and Drag available for multitude of profiles (Naca, Gottinger, FFA,…) so…NEED to relate the flow over the moving airfoil to that of the stationary tests  Relative velocity over the airfoil.  Induction factors
Beta  Angle Drag<->Axial Force and also  Angle Lift<->Tangential Force, since Drga and Lift are based in these factors.
4. Blade Elements
(Forces on the turbine blade)
Sigma prima=LOCAL SOLIDITY: number blades x thickness / (2*PI*r)

## Slide 29
11
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
LCoE [₤/MW-h]
Capacity Factor [%]
CAPEX [₤]
Revenues [₤]
Discounted Profit [₤]
Payback [years]
Project Life [years]
5
Techno-Economic Analysis Tool
Outputs
Tool 4
Tool 5
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
↓LCoE
28
Notes: Blade Element Momentum Theory equates two methods of examining how a wind turbine operates. The ﬁrst method MOMEMENTUM METHOD is to use a momentum balance on a rotating annular stream tube passing through a turbine. The second BLADE ELEMENT METHOD is to examine the forces generated by the aerofoil lift and drag coefﬁcients at various sections along the blade. These two methods then give a series of equations that can be solved iteratively.
a=(v1-v2)/v1 (AXIAL INDUCTION FACTOR)
Momentum method……………………………..
1. Axial Force
(Axial Stream tube around a Wind Turbine)
Bernouilli eq AND p1=p4, V2=v3  AXIAL FORCE on the blade
2. Rotating Annular Stream tube
(Rotating Annular Stream tube)
Conservation of angular momentum in the annular stream tube FOR the 4 stations where, blade rotates at GAMMA mayus  TANGENTIAL FORCE on an annular element of fluid  Torque (T) = tangential force * radius
+Tip Lost Correction (At the tip of the turbine blade losses are introduced in a similar manner to those found in wind tip vorticies on turbine blades)
Blade element method…………………..
3. Relative Flow
(Forces on the turbine blade)
Lift and Drag available for multitude of profiles (Naca, Gottinger, FFA,…) so…NEED to relate the flow over the moving airfoil to that of the stationary tests  Relative velocity over the airfoil.  Induction factors
Beta  Angle Drag<->Axial Force and also  Angle Lift<->Tangential Force, since Drga and Lift are based in these factors.
4. Blade Elements
(Forces on the turbine blade)
Sigma prima=LOCAL SOLIDITY: number blades x thickness / (2*PI*r)

## Slide 30
11
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
5
Techno-Economic Analysis Tool
Tool 4
Tool 5
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Outputs
Aluminium
Stainless Steel
29

## Slide 31
11
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
5
Techno-Economic Analysis Tool
Tool 4
Tool 5
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Methodology
(Cost Study for Large Wind Turbine Blades: WindPACT Blade System Design Studies)
(Issues and Opportunities for Advancing Technology, Expanding Renewable Generation and Reducing Emissions)
Sensitivity Analysis
30

## Slide 32
11
A Decision Support Tool for the Resource, Performance and Survivability Analysis of Tidal Turbines
Diagram
Tool 4
Tool 5
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Wave/Tidal Interaction
Exceedance Curve Calculator
BEM Analysis
Material Analysis
Techno-Economic Analysis
1
2
3
4
5
Drot = 22 [m]
dHUB-SABED = 15 [m]
45 Optimum Blades
Aluminium Alloy
LCoE = 192 [£/MW-h]
Flow Probabilities
31

## Slide 33
Tool 4
Tool 5
Introduction
Tool 1
Tool 2
Tool 3
Conclusion
A Methodology for a Decision Support Tool for a Tidal Stream Device
Reliable
Efficient
Compact
Conclusions
32

## Slide 34
Andrew Cooper
Julen Garcia-Ibanez
Ciaran Gilbert
Stuart Mack
Xabier Miquelez de Mendiluce
A Methodology for a Decision Support Tool for a Tidal Stream Device
29/04/2014
?
A Methodology for a Decision Support Tool for a Tidal Stream Device
?