## Slide 1
Scoping Future Integrated Energy Systems for Findhorn Eco-community
29th April 2014
Arnau Girona
James Copeland
Jamie MacDonald
Laura Rolo
Sophie Vivaudou

## Slide 2
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Eco-village located in the North of Scotland
Current energy situation:
  Annual demand = 1.2 GWh
  Annual generation = 1.65 GWh
Planned Expansion of Eco village
Our Aim: To investigate energy systems at Findhorn Eco-Village and provide scope for future improvements.
Background
Findhorn

## Slide 3
Methodology
Current situation
High Demand
Unused on-site generation
Heating system improvement
Generation
Storage
Supply Demand Match
Increment of demand
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 4
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
How can thermal storage be used for load shifting and demand reduction?

## Slide 5
Variety of Heating Systems at Findhorn
Our Focus refined to Centini houses
They present load reduction and shifting opportunities because:
1) Large storage tanks
2) Solar thermal technology
3) Electric immersion back Up
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Thermal Systems at Findhorn
Woodstoves
Biomass Boilers
Solar Thermal Panels

## Slide 6
Storage capacity varies depending on temperature that tank is heated to
Approximate losses of < 0.4°C per hour but dissipated as heat in house. (Useful in winter)
Plenty storage potential to pre-charge tank during night or excess wind generation and then “coast” on this energy, avoiding future electrical load for heating
Load Shifting Utilising Thermal Storage
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 7
We analysed monitored data from Findhorn
From graph we can observe: 1) Solar gain
2) Losses
3) Shifting ability of regular significant load (red line)
Load Shifting Utilising Thermal Storage
Shifting Options | Immersion Timing Before and After Shift to Night time (off peak) | To match with excess wind
Winter | 07:00 →9:30 & 19:00 → 21:30 23:30 → 5:00 | ?
Summer | 06:00 →07:30 00:30 → 04:00 | ?
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 8
We Investigated a verified C# Program and modified the code to suit systems at the Centini houses
Example of programme display below
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Demand Reduction using Controls

## Slide 9
We programmed specific draw profiles weather data and tank specifications
Programme gives output of auxiliary energy use and solar factor
Model shows that auxiliary use can be reduced with the use of an intelligent control system
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Demand Reduction using Controls

## Slide 10
Example template of hypothetical user display
Solar Thermal controls and various weather predictions can be communicated to user for increased control and management
Area for future development alongside improved Solar Thermal controls
Incident Radiation (w/m^2)
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Demand Side Management

## Slide 11
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
What kind of new generation system can be used ?

## Slide 12
Technology | Predictable | Steady | Low EI | Costs | Scale | Grid Connection | Enough Power output
Onshore wind |  |  |  |  |  |  | 
Offshore wind |  |  |  |  |  |  | 
Microhydro |  |  |  |  |  |  | 
Tidal Barrage |  |  |  |  |  |  | 
Wave |  |  |  |  |  |  | 
Tidal stream |  |  |  |  |  |  | 
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
New Generation Options

## Slide 13
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Findhorn Bay

## Slide 14
Tide Data Surface Speed |  |  |  |  | 
Times | Neaps (knots) | Springs (knots) | Direction | Neaps (m/s) | Springs (m/s)
Hw-6 | 0 | 0 | Slack | 0.00 | 0.00
Hw-5 | 0.2 | 0.4 | W | 0.10 | 0.21
Hw-4 | 0.3 | 0.8 | W | 0.15 | 0.41
Hw-3 | 0.5 | 0.9 | SW | 0.26 | 0.46
Hw-2 | 0.3 | 0.7 | SW | 0.15 | 0.36
Hw-1 | 0.3 | 0.5 | SW | 0.15 | 0.26
Hw | 0.3 | 0.6 | SW | 0.15 | 0.31
Hw+1 | 0 | 0 | Slack | 0.00 | 0.00
Hw+2 | 0.2 | 0.4 | E | 0.10 | 0.21
Hw+3 | 0.5 | 0.9 | E | 0.26 | 0.46
Hw+4 | 0.6 | 1.1 | NE | 0.31 | 0.57
Hw+5 | 0.3 | 0.7 | NE | 0.15 | 0.36
Hw+6 | 0.2 | 0.3 | NE | 0.10 | 0.15
 | Tide Heights in meters above datum |  |  |  |  | 
Place | Lat N | Long W | MHWS | MHWN | MLWN | MLWS
Burghead | 57º 42’ | 3º 30’ | 4.1 | 3.2 | 1.6 | 0.6
Nairn | 57º 36’ | 3º 52’ | 4.3 | 3.3 | 1.6 | 0.7
Findhorn | 57º 40’ | 3º 39’ | 4.2 | 3.25 | 1.6 | 0.65
20 m3/s
Historical Data
Max!!
Admiralty Tidal Stream Atlas
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Tidal Resource

## Slide 15
Site Survey
Measurements
State of Tidal and Moon
Locations
Spring Tide Current
2.11 m/s
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Tidal Resource

## Slide 16
Tidal Harmonic constituents – Aberdeen Port Date span 89-07 |  |  |  |  | 
Constituent | Period (hr) | Period (s) | Amplitude (m) | Frequency (Rad/s) | Phase (Rad)
O1 | 25.8 | 92880 | 0.127 | 0.24 | 51.10
K1 | 23.93 | 86148 | 0.113 | 0.26 | 204.56
M2 | 12.42 | 44712 | 1.301 | 0.51 | 24.57
S2 | 12 | 43200 | 0.44 | 0.52 | 62.88
Tiidal form number |  | 0.137 | Semidiurnal tide |  | 
Chart: Days
Chart: Days
Chart: Power Density (kW/m2)
Exceedance Curves
APD = 1.25 kW/m2
Vrmc = 1.08m/s
Neap Tide
Spring Tide
Vneap = 0.74m/s
Vspring = 2.2m/s
Chart: Velocity (m/s)
| 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1 | 1.05 | 1.1000000000000001 | 1.1499999999999999 | 1.2 | 1.25 | 1.3 | 1.35 | 1.4 | 1.45 | 1.5 | 1.55 | 1.6 | 1.65 | 1.7 | 1.75 | 1.8 | 1.85 | 1.9 | 1.95 | 2 | 2.0499999999999998 | 2.1 | 2.15 | 2.2000000000000002 | 2.25
Velocity | 0.0026882 | 0.024194 | 0.019489 | 0.024194 | 0.020161 | 0.019489 | 0.025538 | 0.016801 | 0.024194 | 0.016129 | 0.028898 | 0.019489 | 0.015457 | 0.02621 | 0.024194 | 0.025538 | 0.03293 | 0.024194 | 0.026882 | 0.030914 | 0.027554 | 0.022849 | 0.027554 | 0.023522 | 0.031586 | 0.02621 | 0.032258 | 0.026882 | 0.022849 | 0.025538 | 0.020161 | 0.023522 | 0.022177 | 0.021505 | 0.024194 | 0.016129 | 0.024194 | 0.013441 | 0.023522 | 0.024194 | 0.016129 | 0.016801 | 0.018145 | 0.010753 | 0.0073925 | 0.0033602
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Harmonic Analysis

## Slide 17
Floating
Vertical Axes
Small Scale
Average Monthly = 317.24 kW
Cut-in
Cut-out
Average Day = 10.23 kW
Annual Energy = 37.20 MWh
Power Output
Chart: Water Velocity (m/s)
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Tidal Stream Device

## Slide 18
Environmental Concerns
Barrier Effects on movement and Migration
Displacement
Underwater Collision
Underwater Noise
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Project
Chart: 

## Slide 19
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
What kind of electricity storage system can be used ?

## Slide 20: Introduction
Inquiry about a suitable and feasible electrical storage system.
Objective
Why integrate Storage in communities?
Increase use of own generation
Decrease dependency to grid ( “Non- clean” energy)
Economical aspects
Can be seen as a big load shifting
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 21: Technologies
 | Efficiency | Lifetime | Approx. Cost (£/kWh) | Advantages | Disadvantages
Battery (classical Lithium-ion) | 0.7-0.75 | 10-15 years | 400-1400 | -High efficiency -Mature Technology | -Need for thermal regulation -Cost -Rare material used
Redox Flow Battery | 0.65-0.75 | 15-20 years | 100-400 | -High modularity -Large range of Power -High rate of discharge -Lifetime | -Complex architecture -Maintenance cost -“New” technology -Risk of leak in the electrolyte -Vanadium and sulphuric acid
Hydrogen Storage | 0.25-0.35 | 5-10 years | <400 | -Clean fuel -Abundant resource | -Low efficiency - Technical problems with storage and transport -Cost
Compressed Air Energy Storage (CAES) | 0.4-0.5 | 30-40 years | 100-200 | -Clean fuel -High power, high capacity -Simplicity -Lifetime -Mature technology | - “Low” efficiencies -Noise ????
What technology could be used?
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 22
EES Analysis
Gas cycle analysis in EES software:
1
5
3
4
2
Wc
Wt
T_w2
T_w1
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 23
System proposed
Future work
Capacity: 1400kWh
Efficiency = 58% in theory + CHP opportunity
Power output can be adapted
2 Compressors from SAUER compressor:
    200 bars
    32 kW rated power
    Water cooled
Storage tank
    200 bars
    185 m3 (2m radius,15 m long)
Experimentation
Isothermal compression
≈£200,000
Expansion stage
Cost effective solution
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology

## Slide 24
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
How the solutions studied influence the Supply and Demand match?

## Slide 25
A 750 kW wind farm:
3 Vestas V29 225kW
1 Vestas V17 75kW
Demand | Generation | Surplus | Deficit
1.2 GWh | 1.65 GWh | 858.27 MWh | 410.55 MWh
Generation
Demand
Installed
Meters
Winter
week
Summer
week
Annual Analysis
Week Analysis
SDM analysis using Merit software
Power (KW)
Power (kW)
Time (Hours)
Time (Hours)
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Initial Scenario

## Slide 26
Time (Hours)
Winter week demand profile
Summer week demand profile
Initial
Scenario
Modified
Profile
Annual Analysis
Demand | Demand | Surplus | Deficit
Initial | 1.19 GWh | 858.27 MWh | 410.55 MWh
Modified HS | 1.14 GWh | 895.90 MWh | 393.41 MWh
Improve heating system in 10 houses:
Thermal solar panels + electric backup
Storage tank – shift loads
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Time (Hours)
Time (Hours)
Time (Hours)
Deficit Reduction: 17MWh
Power (kW)
Power (kW)
Power (KW)
Power (kW)
Demand Reduction: 50MWh
Heating System

## Slide 27
Generation | Demand | Generation | Surplus | Deficit
Wind | 1.19 GWh | 1.65 GWh | 858.27 MWh | 410.55 MWh
Wind & Tidal | 1.19 GWh | 1.85 GWh | 968.90 MWh | 316.41 MWh
Month Analysis
Demand
Generation
Annual Analysis
Generation
Increase: 200MWh
Deficit Reduction: 94.14MWh
Peak Power
100 kW
4 turbines: 25 kW rated Power
Peak Power
240 kW
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Tidal Generation

## Slide 28
Storage | Surplus | Deficit
NULL | 858.27 MWh | 410.55 MWh
CAES - 900 kWh - 60kW | 750.86 MWh | 326.75 MWh
CAES - 1.5 MWh- 60kW | 721.72 MWh | 305.01 MWh
CAES - 1.5 MWh- 120kW | 688.46 MWh | 284.30 MWh
Annual Analysis:
Week Analysis: – Initial Scenario
Model CAES:
Capacity: 900kWh – 10 MWh
Discharge time: 12 hours (max. power)
Charge power 60 kW – 120kW
Surplus
Deficit
Week Analysis – Storage: 1.5MWh – 60kW
Week Analysis – Storage: 10MWh – 120kW
State of charge (%)
Deficit Reduction: 105MWh
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Electricity Storage

## Slide 29
Technology | Benefits/ year | Life time | Installation cost | Payback period | Deficit reduction | Conclusions
Thermal (10 houses) | £5,710 | 25 Years | £50,000 | 8.7 Years | 5% | Economic benefits Demand reduction No significant deficit reduction
Tidal | £23,000 | 20 Years | £196,000 | 8.5 Years | 23% | Economic benefits Generation Increase Significant deficit reduction
Storage | £2,340 | 40 Years | £200,000 | 85 Years | 25% | Expensive Significant deficit reduction
Intro
Thermal
Generation
S&D Match
Storage
Conclusions
Methodology
Conclusions

## Slide 30
Acknowledgments:
Supervisor Paul Tuohy
Findhorn Foundation: Vera, Michael, Paddy, Mari.
Findhorn Marine: Pippa.
University of Strathclyde staff.
SAUER Industrial compressors.