## Slide 1
– TETHYS –
Innovative Floating Multi-Purpose Marine Renewable Energy Platform
Team Members
Alasdair Fulton, Giacomo Politi, Ignacio Alvarez Freire, Ioannis Tsichlis, Theofanis Katsoulis

## Slide 2
Introduction
Project Aim
Investigate the reduction of LCOE in floating renewable energy farms
Motivate industry to move far from shore into deep waters

## Slide 3
Introduction
Why Far from Shore into Deep Waters?
Opportunity for Wind & Wave Synergy
Limitations with Fixed Structures
Near-Shore Shallow Sites Developed/Leased
Enormous Wind & Wave Resources

## Slide 4
The Project
Introduction
TETHYS Platform
Floating Wind Farm

## Slide 5
Deep Sea – Far from Shore

## Slide 6
Floating Wind Farm
How to support O&M reducing the cost
  O&M cost = 25% of LCOE
How to reduce Lifecycle Cost?

## Slide 7
TETHYS
Multi-Purpose Platform
Floating Wind Farm
How to support O&M reducing the cost
  O&M cost = 25% of LCOE
How to reduce Lifecycle Cost?

## Slide 8
Pneumatically Stabilized Platform

## Slide 9
Oscillating Water Column Integrated Wave Device

## Slide 10
2x Integrated Wind Turbines

## Slide 11
Substation
Personnel Accommodation

## Slide 12
Operations & Maintenance Facilities
Offshore Assembly Workshop

## Slide 13
Calm-side for safe Vessel Mooring and Equipment Transfer

## Slide 14
Other Purposes/Uses
Research Facilities
Aquaculture Facilities
Introduction
Offshore Electrical Network Connection Hub

## Slide 15
Objectives
Feasibility of Tethys Concept
Levelised Cost of Electricity (LCOE) Calculation
Introduction
LCOE Comparison with Mothership

## Slide 16
What’s next?
Wind & Wave Synergy
Location
Technical Analysis
Financial Analysis
Introduction

## Slide 17
Wind & Wave Synergy
Steady output - 80:20 ratio
Complementary energy sources
Area optimization
Wave subsidies
Mix of Wind & Wave
Notes: Swell & Wind Decoupled – Average Output Smoothed
Optimum Ratio

## Slide 18
Major wave resource
  30 - 40 kW/m
Major wind resource
  10 m/s
Depth
  95 - 120 m
Site Selection
Location
Grid Connection Point Dounreay (275 kV)

## Slide 19
Grid Connection
Cable Arrangement – Key Challenge
Export Cable (132 kV)
Distance > 75 km from shore > HVDC
Commercial availability: ABB & Siemens
DC to reduce losses
Inter-array cables (33 kV)
Moored at specific points – umbilical cables
PSP & WTG Units floating > Dynamic cables
HVAC

## Slide 20: Transformation 33 kV AC 132 kV DC
Grid Connection
Offshore Substation
Capacity >100 MW
Distance from Shore >75 km

## Slide 21
Windfarm
WT Distance
1,200-1,400 m
Radius mooring lines
700-900 m
Windfarm/WEC - Specifications
FLOAT INCORPORATED
Wave Energy Converter
28.8 MW
SIEMENS SWT-6.0-154
Wind Turbines
6 MW

## Slide 22
191°
Lay-Down Area
50 m
200 m
1000 m2
SS
C
A
WEC Power Take-Off
WS
H
R
A = Accommodation
SS = Substation
WS = Workshop & Stores
C = Crane
H = Helipad
R = Research Centre
Design Feasibility
TETHYS Layout
720 m

## Slide 23
Hydrostatics Model Design
Design Feasibility

## Slide 24
Design Feasibility
M
G
K
B
Keel
Center of Gravity
K
G
Center of Buoyancy
Metacenter
B
M
Hydrostatics Parameters

## Slide 25
Design Feasibility
Design Feasibility
Metacentric Height > 0
35.7 m > 0
Displaced weight of water = total weight of the structure
333,512 Tons
Hydrostatics Results - Floating Conditions

## Slide 26
Wave Energy Collector and PSP
Integrated Design
Capacity Coefficient = 41%
Tuned to Absorb Waves Across Spectrum
No Moving Parts Under Water
50-70%
~20-25%
Incoming Waves
Calm Side
Design Feasibility

## Slide 27
Design Feasibility
Hydrodynamics Model
Meshed design of the platform using MaxSurf

## Slide 28
Hydrodynamics - JONSWAP Inputs
Design Feasibility
Maxsurf Used to Analyse 6 Sea States
6 Degrees of Freedom Analysed
0.3 m to 7.5 m
Analysis using the JONSWAP Spectrum - location based
Heave
Pitch
Roll
Sway
Surge
Yaw

## Slide 29
Hydrodynamics Results
Design Feasibility
Heave
Chart: Metres
| Sea State 2 | Sea State 3 | Sea State 4 | Sea State 5 | Sea State 6 | Sea State 7
Wave Height (Hs) | 0.3 | 0.88 | 1.88 | 3.25 | 5 | 7.5
Platform Motion (Heave) | 0.011 | 0.038 | 0.088 | 0.205 | 0.752 | 1.904

## Slide 30
Cost Analysis
Cost Analysis: Levelised Cost of Electricity
Wind Turbine CAPEX
Wind Turbine OPEX
Platform CAPEX
Platform OPEX
Distance to Shore = 75 km
Water Depth = 100 m
Platform Size = 720 m
Number of Turbines (Variable)
LCOE £ per MWh
WEC High / Low
TETHYS vs Mothership
SENSITIVITY
Fixed Inputs
Project Specific Inputs
Wind Turbine Energy Yield
Platform
Energy Yield

## Slide 31
Cost Analysis: TETHYS LCOE - Wind & Wave Synergy
Industry Leading WEC
FLOAT Inc. L-Shaped OWC
Cost Analysis
15%
20%
80%
6 x 6 MW WTs
41%
16 x 6 MW WTs
172 GWh/yr
461 GWh/yr

## Slide 32
Cost Analysis: LCOE Wind & Wave Synergy
60% Loss
22% Profit
£296/MWh
£144/MWh
Cost Analysis
27%
£182
Break Even

## Slide 33
Cost Analysis: LCOE TETHYS vs Mothership
Wind Strike Price £155/MWh | Wave Strike Price £305/MWh
Scenarios
& Sensitivities
Low Case:
WEC 15% Cap. Coef.
High Case:
WEC 41% Cap. Coef.
Comparison:
Mothership
Cost Analysis

## Slide 34
Cost Analysis: Profit TETHYS vs Mothership
Wind Strike Price £155/MWh | Wave Strike Price £305/MWh
Profit
WEC Strike Price £305/MWh
WIND Strike Price £155/MWh
High (41%) Case More Profitable
Cost Analysis
Profit (Discounted)

## Slide 35
Cost Analysis: TETHYS vs Mothership
Based on 50 Wind Turbines
Wave Energy Sales Contribute 17% in High Case (7% in Low)
Wave-Wind 8:100
Cost Analysis
Comparison

## Slide 36
Conclusions - Financial
Conclusions
Profitable and Technically Viable
Competes with Mothership
Wave Energy Extraction Feasible
Improved Profitability
Economics Influenced by Platform CAPEX & WEC Performance
Optimisation Required

## Slide 37
Conclusions - Overall
Conclusions
Stabilised, Comfortable,
Multi-Use Platform
Reduced Motion, Improved Safety
Wind & Wave Combined
Future Grid Benefits
Supports Wind Farm Expansion and Additional Renewable Farms
Expandable

## Slide 38
Any Questions?