## Slide 1: NRCan modules for ESP-r ”Hot” Modules added to support the Canadian housing stock
Lukas Swan – Dalhousie Univ.

## Slide 2: HOT Modules for ESP-r
Per Building (1 for all zones)
  *aim – AIM2 Alberta Infiltration Model (leaks)
  *mvnt – Mechanical ventilation model (air exchange systems)
  *bcd – Boundary condition file (timestep information of draws, electrical loads, etc.)
  *pnt – Electrical network file for type 18 (A&L loads)
  *hvac – HVAC equipment calcs model (primary energy consumption)
  *dhw – Simple DHW model for primary energy consumption
Per Zone
  *bsm – BASESIMP foundation heat loss model

## Slide 3: Ways to find info
Use HOT3000 and examine the your_hot3000_dir\user\wizardhouse
Read some of NRCan’s internal documents (request)
Read the ESP-r source code
  src/cetc
  src/esrubld
  src/esrucom
Examine exemplars
  tester/
NOTE: find most options through HOT program suite (I like HOT2XP as HOT3000 does not have all options)

## Slide 4: Unfortunate things
Not tagged format
Data lines change with system type
Order is important
Some files require others
Most are rudimentarily hacked in
  Problem areas: multi-zone, overrides, etc.

## Slide 5: *.cfg – declare the files
Building
  *aim
  *mvnt
  *dhw
  *hvac
  *bcd
  *pnt
Zone
  *bsm
Order is not important
Requirements:
  HVAC->AIM
  AIM->MVNT
I forgot *selr

## Slide 6: *aim – zone air infiltration
Wind and Stack effect
  Leakage
  Terrain
  Height
  Flues
  Zones
Apportions infiltration to zones
  NOTE: overrides all *.opr infiltration
Applies constant infiltration to crawl and attic (0.5 AC/h)
Supplies temperature data for window opening
  NOTES:
    Requires cooling
    Requires AFN
Affects the infiltration variables in src/esrubld/subsys.F – look up
See: src/cetc/aim2_*timestep.F

## Slide 7: *mvnt – mechanical ventilation
Mech. Ventilation characteristics
  HRV
  CVS
  Exhaust fans
Adds air change to AIM2
Requires *.aim file so that this is executed
Affects the infiltration variables in src/esrubld/subsys.F
See: src/cetc/CentralVentSys.F

## Slide 8: *bcd – boundary condition data
Supplies timestep data
Use: fGet_BC_Data to access
Examples
  Plug loads
  DHW draw
NOTE: Does not interpolate so data must be same/finer than timestep
See: src/esrubps/BC_data.F

## Slide 9: *pnt – electrical network file
Connect Plug loads to electrical from BCD
Type 11/18 to manifest as heat in /src/esrubld/casual.F
Define
  1 node
  Type 18 – Power only component resulting in heat
NOTES:
  Somewhat columnar format
  Provide elec results file *selr
See: src/esrupfs/powoc_calc.F

## Slide 10: *hvac – heating and cooling only!
Systems
  Furnace
  Boiler
  Baseboard
  ASHP
  GSHP
Energy source
  Electricity
  Natural gas/propane
  Oil
  Wood
Old/New version
NOTE: requires simple controller with heating specified
Systems must be in order
  Furnace/boiler/baseboard – including backup
  HP heating
  HP cooling
Resets your simple controller capacity (*.ctl)
Postprocesses to determine primary energy consumption
See: src/cetc/hvacsim.F
  Furnace.F, GCEP.F, ashp.F, baseboard.F

## Slide 11: *dhw – simply to include in consumption
Occupants controls the draw
Single hardcoded profile
Basic tank info
  Type
  Energy source
Postprocesses energy consumption
NOTE: if you open model in prj, it will forget dhw link
See: src/cert/DHW_module.F

## Slide 12: *bsm – foundation heat loss
Dimension and RSI
Moore model (DHW too)
Adjust other files
  Geo: BASESIMP
  Con
    Facing 6
    Type of found.
    % allocation
Walkouts
NOTE: overrides typical heat trans calc
See: src/esrubld/basesimp.F