## Slide 1: An Introduction to ESP-r
Notes: <number>

## Slide 2: Objectives
How does ESP-r model buildings?
What is ESP-r capable of?
How do I model buildings in ESP-r?
Notes: <number>

## Slide 3: Outline
Introduction
  What is Building simulation
  ESP-r methodologies
  ESP-r structure
Demonstration and hands-on exercises
  Building thermal domain
  Network air flow modelling
Notes: <number>

## Slide 4: What is building simulation?
Building Performance
  Equipment sizing
  Energy use & emissions
  Occupant comfort
  Air quality
  Daylighting
  Water management
  Acoustics
Supports integrated design and optimization
CMHC “Healthy House”, Toronto
Notes: <number>

## Slide 5
Image: Clarke, J.A. (2001) Energy Simulation in Building Design, 2nd Edition
Notes: <number>

## Slide 6: Levels of resolution
Feasibility
analysis
Residential
Commercial
Research
US DOE Software tools directory:
http://www.eere.energy.gov/buildings/tools_directory/
RETScreen
Hot 2000
Hot 3000
eQuest (DOE 2.1)
EnergyPlus
TRNSYS, ESP-r
(Easy-to-use)
(Hard-to-use)
Notes: <number>

## Slide 7: ESP-r: Open source software
ESP-r is free software:
  Licensed under the GPL
  “Share-and-share-alike”
Used around the world
Contributions from:
  U.Eidenhoven, U.London, NRC, Concordia, U. Calgary, Dalhousie, U. Toronto, Carleton, Laval, Ecole Polytechnique …
Notes: <number>

## Slide 8: ESP-r: Research focused
ESP-r is a research tool:
  Developed by graduate students and professors
  30-years of development
  “First-principles” philosophy
Ease-of-Use is not a priority:
  Developers are research-focused
  Limited resources for general improvements
  X11 interface circa 1989
  Full of surprises (bugs)
Expect to be frustrated!
Notes: <number>

## Slide 9: ESP-r: X11 interface

## Slide 10: ESP-r: HOT3000
Notes: <number>

## Slide 11: ESP-r: Daylight 1-2-3
Notes: <number>

## Slide 12: ESP-r: Capabilities
Building envelope
Intra-zone air flow (CFD)
Inter-zone air flow
HVAC Systems
Electrical
systems
Acoustics
ESP-r
Indoor Air quality
Renewable Energy
Mold growth
Insolation & obstructions
Radiance (daylighting)
TRNSYS Models (HVAC)
Matlab (controls)
Notes: <number>

## Slide 13: ESP-r: Maturity
Building envelope
Intra-zone air flow (CFD)
Inter-zone air flow
HVAC Systems
Electrical
systems
Acoustics
ESP-r
Indoor Air quality
Renewable Energy
Mold growth
Insolation & obstructions
Radiance (daylighting)
TRNSYS Models (HVAC)
Matlab (controls)
Notes: <number>

## Slide 14: ESP-r: Building domain
ESP-r’s heat-balance method:
  Discretize in space by representing building fabric and internal zones with control volumes (CV).
  Form heat balances for each CV.
  Simultaneously solve matrix of heat balances.
Notes: <number>

## Slide 15: ESP-r: Windows
Notes: <number>

## Slide 16: ESP-r: Integrating other domains
Plant (HVAC)
Air Flow
Power flow
Notes: <number>

## Slide 17: ESP-r: Additional capabilities
  Solar shading.
  Solar insolation.
  Internal surface convection.
  View factor calculation.
  Casual gains control (daylight control).
  Temperature-dependent material properties.
  Image rendering.
  Controls: network air flow, setbacks, etc.
  Plant injections: radiant-slabs, convective heating, convective-radiative, etc...
  Control of optical properties.
  TRNSYS coupling
Notes: <number>

## Slide 18: ESP-r: Explicit plant model
Notes: <number>

## Slide 19: ESP-r: Integraded CFD
Notes: <number>

## Slide 20: ESP-r: Lighting simulation with Radiance
Notes: <number>

## Slide 21: ESP-r: Structure
Project management facility
Simulation engine
Results recovery & analysis
3rd party graphing &
analysis package
3rd party CAD
Plant component db
Event profiles db
Climatic time-series db
Temporal definitions db
Shading/insolation db
Plant component db management
Event profile db management
Climate db analysis & management
Temporal def’ns db management
External shading and internal
insolation prediction
Stand-alone mass flow solver
& results recovery
Problem
description
Mass flow
results
Results database
Export
Notes: <number>

## Slide 22: ESP-r: Availability
Binary versions can be downloaded from:
http://esru.strath.ac.uk
Source code available through versioning control:
http://www.esru.strath.ac.uk/Programs/ESP-r_central.htm
Notes: <number>

## Slide 23: ESP-r: Resources
Documentation:
http://www.esru.strath.ac.uk/
Support mailing list:
http://www.esru.strath.ac.uk/Programs/user_club.htm
Notes: <number>

## Slide 24: Demonstration and exercises
Building domain exercise:
  Defining constructions
  Defining geometry
  Attributing surfaces
  Adding windows
  Applying boundary conditions
  Imposing air flow and internal gains
  Modeling plant and controls ideally
  Adding obstructions
  Performing simulations
  Analyzing results
Notes: <number>

## Slide 25: Constructions databases
Database of construction elements:
  conductivity, density, and specific heat;
  infrared emissivity and solar absorptivity;
  contains many standard materials;
  easily modified.
Database of multilayer constructions:
  layer-by-layer description;
  references materials from elements database;
  specify thickness of each layer.
Notes: <number>

## Slide 26: Opaque envelope
Demonstration and exercise
Notes: <number>

## Slide 27: Defining geometry
Explicit geometrical model required for:
  Inter-surface radiation exchange.
  Internal surface convection.
  Forced external convection.
  Solar shading and insolation patterns.

Notes: <number>

## Slide 28: Defining geometry: creating a zone
Define coordinates of vertex points.
Join vertices to form surfaces.
Zone must be completely enclosed.
Lots of handy tools to assist data input.
Simpler models are better!
Notes: <number>

## Slide 29: Defining geometry: Creating a building
Building defined zone-by-zone.
Zones can be moved, copied, deleted, and merged.
Plan the model (make a sketch) before attempting data input.
CAD input possible, but generally easier to use project manager.
Avoid unnecessary complexity.
Notes: <number>

## Slide 30: Defining Geometry
Demonstration and exercise
Notes: <number>

## Slide 31: Opaque envelope: Attribute surfaces
Surfaces attributed by assigning multilayer constructions from database.
Notes: <number>

## Slide 32: Catch-up
If you did not complete the geometrical input, then do the following:
  Exit ESP-r.
  Enter “skipto intro2” in your terminal.
Notes: <number>

## Slide 33: Windows
Called transparent multilayer constructions.
Created in similar fashion as opaque mlc’s, but:
  optical properties also required;
  gas fill characterized by a thermal resistance.
Can import optical properties from Window.
Create wall geometry first, then insert windows.
Frame: declare separately as opaque MLC or include effect on window U-value and optical properties of window
Notes: <number>

## Slide 34: Windows
Demonstration and exercise
    Insert window w1.
    Attribute the window with the layered construction called d_glz.
Notes: <number>

## Slide 35: Catch-up
If you did not complete the windows input, then do the following:
  Exit ESP-r.
  Enter “skipto intro3” in your terminal.
Notes: <number>

## Slide 36: Applying boundary conditions
Multilayer constructions have inside and outside surfaces.
Notes: <number>

## Slide 37: Types of boundary conditions
The inside surface
  faces the zone’s air-point;
  is handled automatically.
Must define boundary condition for outside surface
  exposed to outdoors;
  faces another zone;
  exposed to fixed temperature and radiation source;
  connected to ground (user-defined monthly temperature profile);
  exposed to same conditions as inside;
  adiabatic;
  BASESIMP foundation.
Notes: <number>

## Slide 38: Applying boundary conditions: Tools
Two approaches:
  Manual method
    Assign boundary condition to each surface the same way it is attributed with a multilayer construction.
  Automatic method
    Use topology checker program to automatically match common surfaces between adjoining zones and prompt for other boundary condition types.
Notes: <number>

## Slide 39: Applying boundary conditions
Demonstration and exercise
  Connect windows, walls and ceiling to exterior.
  Connect floor to BASESIMP, and use configuration 42.
Notes: <number>

## Slide 40: Catch-up
If you did not complete the boundary condition input, then do the following:
  Exit ESP-r.
  Enter “skipto intro4” in your terminal.
Notes: <number>

## Slide 41: Imposing internal gains
Internal gains can be set for:
  occupants;
  lights;
  equipment.
Setting internal gains:
  loads in W or W/ m2;
  radiant and convective portions;
  sensible and latent portions.
Gains are scheduled:
  possible to import fractional profiles from previously created database.
Notes: <number>

## Slide 42: Imposing air flows
Two methods for handling air flow:
  explicitly calculated with a network air-flow model (coming later);
  thermal impact of imposed flows calculated.
Infiltration is air flow from the outdoors to the zone.
Ventilation is air flow from another zone (or at a set temperature).
Notes: <number>

## Slide 43: Imposing air flows
Setting infiltration and ventilation rates:
  on zone-by-zone basis;
  in ac/h (receiving zone);
  scheduled;
  + source zone (or temperature) for ventilation.
Flow rates can be controlled (3-stage) as a function of:
  zone temperature;
  adjacent zone temperature;
  outdoor temperature;
  wind speed.
Notes: <number>

## Slide 44: Imposing air flows and internal gains
Demonstration and exercise
Notes: <number>

## Slide 45: Catch-up
If you did not complete the operations input, then do the following:
  Exit ESP-r.
  Enter “skipto intro5” in your terminal.
Notes: <number>

## Slide 46: Modelling plant and controls Ideally
Two methods for plant modelling:
  explicitly with a component model;
  ideally.
Ideal plant modelling:
  control behavior of HVAC system modeled, but not components;
  usual approach employed by ESP-r users.
Notes: <number>

## Slide 47: Ideal control: Sensor and actuator
Locate sensor:
  current zone temperature;
  air temperature in another zone;
  mix of zone temperature and MRT;
  outdoor condition: temperature, wind, solar.
Locate actuator:
  air point of current zone (convective heater)
  at a surface
  within a layered construction (radiant slab)
  convective/radiative heater
Notes: <number>

## Slide 48: Ideal control: Control law
Specify control period
Select control law:
  ideal heat injection/extraction with fixed capacities;
  free-floating;
  on/off and 3-position;
  constant volume, variable temperature;
  PID, fuzzy-logic PI-PD, etc.
Specify set points and heating & cooling capacities.
Notes: <number>

## Slide 49: Applying ideal control
Demonstration and exercise
free floating
Notes: <number>

## Slide 50: Catch-up
If you did not complete the inputs for zone controls, then do the following:
  Exit ESP-r.
  Enter “skipto intro6” in your terminal.
Notes: <number>

## Slide 51: Shading and Insolation
Two methods for insolation:
  Specified insolation within zone geometry
    Diffuse treatment
    Insolation to 1 or 2 surfaces
  Shading and insolation module: ish
Shading and insolation module:
  Add obstruction blocks, window reveals, overhangs
  Detailed internal insolation distribution
  Limitations:
    Does not account for self shading
    Crude obstruction geometry
Notes: <number>

## Slide 52: Adding obstructions
Notes: <number>

## Slide 53: Catch-up
If you did not complete the inputs for zone shading and insolation, then do the following:
  Exit ESP-r.
  Enter “skipto intro7” in your terminal.
Notes: <number>

## Slide 54: Performing simulations
Select weather file.
Set period of simulation.
Choose time step.
Simulation toggles:
  sky model, surface convection model, solver data, etc.
Trace detailed output:
  convection coefficients, air flows, etc.
Monitor zone temperatures and plant injections as simulation progresses.
Notes: <number>

## Slide 55: Performing simulations
Demonstration and exercise
  Simulate house with constant set-point temperature.
  Repeat simulation, but use set-back thermostat.
  Simulate from Jan 9-15, 1 hour time step.
  User /usr/esru/esp-r/climate/ottawa.cwec for the weather file.
Notes: <number>

## Slide 56: Analyzing Results
Plot solution variables against time:
  zone, surface, and interstitial temperatures;
  plant injections or extractions;
  infiltration & ventilation loads;
  internal loads; etc.
Create plots of cross-sectional temperatures.
Graph frequency distributions:
  temperatures;
  heat fluxes; etc.
Text output of instantaneous and integrated quantities
Notes: <number>

## Slide 57: Analyzing Results
Demonstration and exercise
  Plot zone temperature and heat injection for constant set-point temperature simulation.
  Repeat for set-back thermostat simulation.
Notes: <number>